## Slide 1
Router
R1
Switch S1
Mid Semester Skills TUE1730 S1 2020
Tutor: Satya Exam Duration: 120 minutes
G0/0/1
S0/1/1
S0/1/0
Router
R3
G0/1
ISP
Router
R4
PC1
PC2
Fa 0/2
Fa 0/24
Network Topology
S0/2/0
S0/1/0
WRT300N
Wireless
Router
Smart
Phone
Fa 0/9
VLAN1
Internet Port
VLAN1
IP address
Wireless
Connection
Router
R2
S0/1/0
S0/1/0
S0/1/1
S0/1/1
Switch S2
G0/0/1
G0/1
Server 0
Server 1
G0/0/0
G0/0/1
Database Server
Loopback0
ISP Serial Link
Fa0
Fa0

## Slide 2
Subnet Name | Size | Allocated Size | Address | Mask | Dec Mask | Assignable Range | Broadcast
VLAN90 R1 | 400 | 510 | 158.25.0.0 | /23 | 255.255.254.0 | 158.25.0.1 - 158.25.1.254 | 158.25.1.255
VLAN100 R2 | 200 | 254 | 158.25.2.0 | /24 | 255.255.255.0 | 158.25.2.1 - 158.25.2.254 | 158.25.2.255
DatabaseLoopback0 | 50 | 62 | 158.25.3.0 | /26 | 255.255.255.192 | 158.25.3.1 - 158.25.3.62 | 158.25.3.63
VLAN1 SwS1 | 20 | 30 | 158.25.3.64 | /27 | 255.255.255.224 | 158.25.3.65 - 158.25.3.94 | 158.25.3.95
VLAN1 SwS2 | 20 | 30 | 158.25.3.96 | /27 | 255.255.255.224 | 158.25.3.97 - 158.25.3.126 | 158.25.3.127
Seriallink1 | 2 | 2 | 158.25.3.128 | /30 | 255.255.255.252 | 158.25.3.129 - 158.25.3.130 | 158.25.3.131
Seriallink2 | 2 | 2 | 158.25.3.132 | /30 | 255.255.255.252 | 158.25.3.133 - 158.25.3.134 | 158.25.3.135
Seriallink3 | 2 | 2 | 158.25.3.136 | /30 | 255.255.255.252 | 158.25.3.137 - 158.25.3.138 | 158.25.3.139
Network Address
158.25.0.0/16
VLSM Design
ISP Serial Link Network Address: 205.25.25.0/30
Server 0: 176.25.0.0/16
Server 1: 186.25.0.0/16

## Slide 3: Tasks, Comments and Marks
1. Do not configure enable passwords OR line console passwords on routers and switches, unless specified by the task.
2. Internal Network VLSM Design provided
3. Message of the Day (MOTD) Banner Configuration (If banners are not configured, then 0 marks for Skills Exam)
You must configure a MOTD Banner, recording your student id, family name and lab time, on all routers and switches, as shown below:
banner motd &
Welcome to Hostname
Your Student Id, Your Family Name, Your Lab Time
&
4. Switch Configuration (10 marks)
a) On switch S1
  create VLAN 90 Accounts
  configure ports 2,3 as VLAN 90 access ports
  configure Port Security, mac address sticky on ports 2,3 max 4, with violation shutdown
b) On switch S2
  create VLAN 100 Sales
  configure port 24 as VLAN 100 as access port
c) On both switches configure G0/1 as a trunk port
5. Network IP Address Configuration (15 marks)
a) Switch Management – on both switches configure an ip address on interface VLAN1 and configure a default gateway
b) Configure ALL router serial and loopback interfaces with ip addresses
c) R1 and R2 Routers
ii) Configure Inter-VLAN routing on G0/0/1
  - R1 configure separate sub-interfaces for VLAN 1 (the management VLAN) and VLAN 90
  - R2 configure separate sub-interfaces for VLAN 1 (the management VLAN) and VLAN 100
  - Configure each sub-interface with an ip address
d) Configure PC1 and PC2 Hosts with specified VLAN:
i) IP address and subnet mask.
ii) Default Gateway IP address.
e) Configure ISP Serial Link IP addresses
f) Configure IP addresses on Server 0 and Server 1

## Slide 4: Tasks, Comments and Marks
6. Routing Protocol Configuration (15 marks)
a) R1 and R2
  RIP V2
  Configure passive-interface as appropriate to avoid sending unnecessary routing information
b) R3
  RIP V2, do not advertise the external network address
  Configure passive-interface as appropriate to avoid sending unnecessary routing information
  Configure default route to ISP Router
  Advertise default route to internal routers
c) ISP Router
  Do not configure RIP
  Only configure a static route (default class B mask) to your internal network
7. Wireless Router Configuration (5 marks)
a) You will configure a Wireless Router that connected to the fixed network infrastructure.
b) You will use the smart phone as the wireless device
c) On WRS1 Wireless Router configure:
i) Internet Port with VLAN 1 IP address
ii) DHCP to provide addresses for smart phone
iii) Do not configure wireless security
8. Access List Requirements for VLANs on Routers (10 marks)
a) Create NAMED Extended ACLs to meet the following requirements:
  R1 Router VLAN90 PCs
    PCs denied HTTP access to ISP Server0 and permitted ALL other access to ISP Server0
    PCs permitted All other access to the Internet
  R2 Router VLAN100 PCs
    PCs permitted HTTP access to ISP Server1 and denied ALL other access to ISP Server1
    PCs permitted All other access to the Internet

## Slide 5: Submission Details
1. Save the Packet Tracer file as StudentIdDayLabTimeRoomMidSemSkills
eg if your student Id is 123456789, Day Tuesday, LabTime 1730, Room ATC329 then the Packet Tracer file name will be:
123456789Tue1730ATC329MidSemSkills
2. You must email your Packet Tracer file to your tutor within 10 minutes of the end of the exam, else you will fail the exam with a final mark of zero.